## Slide 1: St. Charles Parish
Department of Waterworks
August 24, 2026
Greg Gorden

## Slide 2: Water System Modeling: Water Model Progress Update
Completed
  Collected GIS, billing, production, SCADA, and asset data
  Developed system demand estimates from billing and production records
  Built a working preliminary hydraulic model
In Progress
  Comparing model results to SCADA and historical fire-flow data
  Refining pump, tank, pressure, and fire-flow behavior
  Identifying data gaps needed for calibration
Upcoming
  Field testing / pressure recorder data collection
  Final calibration and model documentation
  Model handoff and focused staff training

## Slide 3: Water System Modeling: Why Field Data Matters
While the model is running and producing reasonable system results additional data will enable adjustments to improve system flows and pressures
Additional field pressure and fire-flow data will improve model resolution and confidence in results
Testing will help confirm neighborhood-level pressure and fire-flow capacity
Better calibration supports planning, operations, and future PIAL-related review

## Slide 4: Water System Modeling: Key Insights
The model will provide a comprehensive understanding of:
  Water demands associated with major industrial and commercial developments
  Effects on system demand, pressure, and fire-flow capacity
  The existing finished-water distribution system
  Current water-demand levels across the system
Improved baseline data: New direct water meters and detailed billing records provide model developers with reliable current-demand inputs
Data consistency: Customer billing records align with monthly operating reports (MORs), confirming consistency between finished-water production and system consumption

## Slide 5: West Bank C Plant Filter Media Replacement

## Slide 6: West Bank D Plant Clarifier Upgrade
$2,782,000 contract awarded to Pintail Contracting Services, LLC
The project includes removal and replacement of the water treatment plant’s existing rectangular solids-contact clarifier and softener.
Internal clarifier components will be upgraded from painted black iron to stainless steel, reducing long-term maintenance requirements and costs.
Fabrication of the new internal components is underway, with delivery scheduled for October.
Following delivery, the contractor will have 180 days to complete installation.

## Slide 7: West Bank E Plant Design
$4 million Design over three years ($3 million Capital Outlay Award)
2026 – Conceptual Phase Completion and Start Preliminary Design
2027 – Complete Preliminary Design
2028 – Complete Final Design
Progress to Date:
  Site Survey Complete
  Space usage Program in process
  Electrical Design initiated

## Slide 8: West Bank E Plant Design: Key Drivers
Primary drivers for the design initiative
  Address existing operational and facility constraints
    Motor control panels currently share space with control room and laboratory functions
    Chemical handling, control room, and laboratory functions occupy a common area
    No dedicated bunk room is available for staff pre-positioned during emergencies or severe weather events
  Modernize aging infrastructure
      Existing plant years: A (1958), B (1964), C (1972), and D (1984)

## Slide 9: Slide Title

## Slide 10: Billing and Accounting Process Improvements
Streamlined daily recordkeeping for financial transactions
Established a secure digital records system on the department’s shared drive
Waterworks staff can now retrieve documents in seconds, eliminating time-consuming searches through paper files
Lowered printing expenses while reducing paper use and physical storage needs
Strengthened safeguards against records being lost or damaged during natural disasters and severe storms

## Slide 11: St. Charles Parish
Department of Waterworks
August 24, 2026
Greg Gorden